## Slide 1: Channel Access Push Proposal for a New Connection Method
Dirk Zimoch :: Controls Section :: Paul Scherrer Institut
EPICS Collaboration Meeting at ICALEPCS 2017

## Slide 2: Channel Access Monitor Workflow
Current (simplified) work flow to set up a monitor
What's wrong?
Some “clients” (e.g. archiver) flood the network with broadcasts. Reasons: wrong configuration, IOCs offline, …
Archiver not a client at all, it's a service!
IOC |  | CA Client
Looks up PVs | ← | Searches for PVs (UDP broadcast)
Search response (UDP unicast) | → | Gets host/port from response
Accepts connection | ← | Connects (TCP) to host/port
Installs subscriptions | ← | Set up monitors
Sends PV events | → | Processes data
Goes offline |  | Searches again

## Slide 3: Clients vs Services
CA Client | CA Service
PVs live on IOC | 
IOC sends updates | 
Runs on arbitrary hosts | Runs on well known host:port
Can start and top at any time | Usually runs permanently
Client wants something from IOC | IOC wants something from service
IOC cannot know PVs needed by client: Configuration must be in the client | IOC knows PVs to send to service: Configuration should be in the IOC
Let the IOC push its PVs to the service!
Use info fields in records for configuration
IOC does connection management

## Slide 4: Channel Access Push Workflow
Proposed work flow to send data to services
A Channel Access service would be passive
Service needs no PV list configuration
PV list cannot be outdated
Service does not send search broadcasts
IOC pushes PVs to service
Event/subscription concept and code probably does not change much
“Only” connection setup needs to be developed
IOC |  | CA Service
Connects (TCP) to well known host:port | → | Accepts connection
Sends list of PVs (necessary?) | → | Sets up monitors
Sends PV events | → | Processes data
Goes offline |  | Stops monitoring

## Slide 5: What do you think?
Does this look useful?
Channel Access or PV Access or both?
Anyone volunteering to implement it?