## Slide 1: Current EPICS Developments at PSI
Dirk Zimoch :: Controls Section :: Paul Scherrer Institut
EPICS Collaboration Meeting at ICALEPCS 2017

## Slide 2: IOC Utilities at PSI
Dirk Zimoch :: Controls Section :: Paul Scherrer Institut
EPICS Collaboration Meeting at ICALEPCS 2017

## Slide 3: Goal: Make Life Easier
Simplify tedious work
  Adding new scan rate
  Adding breakpoint tables
  Setting EPICS_CA_MAX_ARRAY_BYTES
Help debugging with reverse lookup functions
  Listing all aliases of a record
  Listing all links pointing to a record
  Listing all CA connections to a record
Accessing info fields
  List matching infos of all records
  Iterator API function to traverse matching infos
  Read infos with Channel Access

## Slide 4: Adding New Scan Rate
Edit menuScan.dbd the right way and rebuild
Or simply execute addScan command in startup script:
    addScan .3
  Automatically calls sysClkRateSet() on vxWorks if necessary
    choice(menuScan_2_second,".2 second") choice(menuScan_1_second,".1 second") }
choice(menuScan_3_second,".3 second")
  menu(menuScan) { choice(menuScanPassive,"Passive") choice(menuScanEvent,"Event") choice(menuScanI_O_Intr,"I/O Intr") # Periodic scans follow, ordered from slowest to fastest choice(menuScan10_second,"10 second") choice(menuScan5_second,"5 second") choice(menuScan2_second,"2 second") choice(menuScan1_second,"1 second") choice(menuScan_5_second,".5 second")
Basically arbitrary name
Defines new scan rate. Up to R3.15: unit must be “second”
    choice(menuScan_2_second,".2 second") choice(menuScan_1_second,".1 second") }

## Slide 5: Adding Breakpoint Tables
Include bpt*.dbd, edit menuConvert.dbd and then rebuild
Or simply load bpt*.dbd files and update menuConvert in startup script
    dbLoadDatabase bptMyConv.dbd dbLoadDatabase bptMyOtherConv.dbd updateMenuConvert
    }
    choice(menuConvertmyConv,"myConv") choice(menuConvertmyOtherConv,"myOtherConv")
  menu(menuConvert) { choice(menuConvertNO_CONVERSION,"NO CONVERSION") choice(menuConvertSLOPE,"SLOPE") choice(menuConvertLINEAR,"LINEAR") choice(menuConverttypeKdegF,"typeKdegF") choice(menuConverttypeKdegC,"typeKdegC") choice(menuConverttypeJdegF,"typeJdegF") choice(menuConverttypeJdegC,"typeJdegC") choice(menuConverttypeEdegF,"typeEdegF(ixe only)") choice(menuConverttypeEdegC,"typeEdegC(ixe only)")
Must match name of breaktable in bpt*.dbd file
Basically arbitrary name
    }

## Slide 6: Setting EPICS_CA_MAX_ARRAY_BYTES
EPICS_CA_MAX_ARRAY_BYTES on IOC too small: array PVs inaccessible
  (Not needed any more with R3.16)
Check size of all array fields of all records
  Keep in mind CA type promotion (e.g. ULONG  DOUBLE)
  Add overhead for status, severity, time stamp, …
  Find maximum
Add to startup script: epicsEnvSet EPICS_CA_MAX_ARRAY_BYTES,…
Or simply calculate it automatically
  Init hook checks potential array fields of all records
    Two SynApps records needed patch for cvt_addr(): sCalcout record and table record
  Sets EPICS_CA_MAX_ARRAY_BYTES if current value (or default) is too small

## Slide 7: Listing All Aliases of a Record
Translating alias name to record name is easy
  Remote: caget aliasname.NAME
  On IOC shell: dbla aliasname
    Works with patterns: dbla *XYZ
Finding all aliases of a record is difficult
  Call dbla without parameter, then search the list
Or modify dbla to accept alias or record name patterns
    > dbla recordname alias1 -> recordname alias2 -> recordname alias2 -> recordname

## Slide 8: Listing All Links Pointing to a Record
Finding link targets of a record is not too difficult
  On IOC shell: dbpr record,4 then search the output for links
  Or get known link field: dbgf record.OUT
Finding all links with a given target record is very difficult
  Analyze record database offline and search for links
Or use new IOC shell function: dbll record-pattern
    > dbll *:X A.DOL --> DEV1:X B.INPA --> DEV2:X.VAL MS CP C.OUT --> DEV3:X.RVAL PP
Filter for target field
    > dbll *:X.VAL A.DOL --> DEV1:X B.INPA --> DEV2:X.VAL MS CP

## Slide 9: Listing All CA Connections to a Record
It is possible to get all CA connections to an IOC
  On IOC shell: casr 2
Good luck searching the output for a specific record!
Or use new IOC shell function: cal record-pattern
    > cal MYRECORD zimoch@pc1234:47643 --> MYRECORD.VAL zimoch@pc1234:47643 --> MYRECORD.EGU archive_user@archive_host:83542 --> MYRECORD.VAL

## Slide 10: Accessing Info Fields
Records can have info fields
    record (ai, "REC1") { info(autosaveFields_pass0, "LOLO LOW LLSV LSV") }
But info fields are not easily accessible
Use new IOC shell function: dbli info-pattern [pattern ...]
    > dbli autosaveFields* REC1.autosaveFields_pass0 "LOLO LOW LLSV LSV" REC2.autosaveFields_pass1 "VAL"

## Slide 11: Accessing Info Fields (cont.)
New iterator API function: dbNextMatchingInfo
    char* patternlist[] = {"autosaveFields*", NULL};
    dbInitEntry(pdbbase, &dbentry); while(dbNextMatchingInfo(&dbentry, patternlist) == 0) { printf("%s.%s \"%s\"\n", dbGetRecordName(&dbentry), dbGetInfoName(&dbentry), dbGetInfoString(&dbentry)); } dbFinishEntry(&dbentry);
Goody: Use Channel Access to read info fields
    $ caget REC1.autosaveFields_pass0 REC1.autosaveFields_pass0 LOLO LOW LLSV LSV
NULL terminated array of pattern strings

## Slide 12: How to get it?
Package with utility functions (everything except Channel Access patch) http://epics.web.psi.ch/software/iocUtils.tgz
Patch for Channel Access to info fields
  for EPICS 3.15 and 3.16 http://epics.web.psi.ch/software/caInfoFields-R3-15.patch
  for EPICS 3.14 http://epics.web.psi.ch/software/caInfoFields-R3-14.patch
I will try to get these changes into EPICS base.

## Slide 13: Extending mbbiDirect and mbboDirect Records to 32 Bit
Dirk Zimoch :: Controls Section :: Paul Scherrer Institut
EPICS Collaboration Meeting at ICALEPCS 2017

## Slide 14: Current mbbiDirect
Input (RVAL) is 32 bit
Output (VAL, B0 … BF) is only 16 bit
Why?
mbbiDirect
RVAL 32 bit
VAL 16 bit
B0
BF
⁞
SHFT
Device support

## Slide 15: Future mbbiDirect
Input (RVAL) stays 32 bit
Output (VAL, B0 … BF, B10 … B1F) will be 32 bit as well
Mostly backward compatible
mbbiDirect
RVAL 32 bit
VAL 32 bit
B0
B1F
⁞
SHFT
Device support

## Slide 16: Same for mbboDirect
Output (RVAL) stays 32 bit
Input (VAL, B0 … BF, B10 … B1F) will be 32 bit as well
mbboDirect
VAL 32 bit
RVAL 32 bit
B0
B1F
⁞
SHFT
Device support

## Slide 17: Compatibility
RVAL was and will be ULONG
  Most device supports only access RVAL and need no change
  Record memory layout changes: re-compile all device supports!
VAL was USHORT and will be LONG
  For 16 bit values nothing will change
  Channel Access Clients have always seen a LONG
Device support accessing VAL or B* fields need modification to support higher bits.
  Use 32 bit variables when accessing prec->val
  Using pointer &prec->val is not safe!
  When iterating bit fields check for macros like mbboDirectRecordB1F

## Slide 18: Why not 64 bit?
64 bit integers are not supported by Channel Access
Changing RVAL to 64 bit would break all existing device support
Possible as new record type
What do you think?

## Slide 19: Channel Access Push Proposal for a New Connection Method
Dirk Zimoch :: Controls Section :: Paul Scherrer Institut
EPICS Collaboration Meeting at ICALEPCS 2017

## Slide 20: Channel Access Monitor Workflow
Current (simplified) work flow to set up a monitor
What's wrong?
Some “clients” (e.g. archiver) flood the network with broadcasts. Reasons: wrong configuration, IOCs offline, …
Archiver not a client at all, it's a service!
IOC |  | CA Client
Looks up PVs | ← | Searches for PVs (UDP broadcast)
Search response (UDP unicast) | → | Gets host/port from response
Accepts connection | ← | Connects (TCP) to host/port
Installs subscriptions | ← | Set up monitors
Sends PV events | → | Processes data
Goes offline |  | Searches again

## Slide 21: Clients vs Services
CA Client | CA Service
PVs live on IOC | 
IOC sends updates | 
Runs on arbitrary hosts | Runs on well known host:port
Can start and top at any time | Usually runs permanently
Client wants something from IOC | IOC wants something from service
IOC cannot know PVs needed by client: Configuration must be in the client | IOC knows PVs to send to service: Configuration should be in the IOC
Let the IOC push its PVs to the service!
Use info fields in records for configuration
IOC does connection management

## Slide 22: Channel Access Push Workflow
Proposed work flow to send data to services
A Channel Access service would be passive
Service needs no PV list configuration
PV list cannot be outdated
Service does not send search broadcasts
IOC pushes PVs to service
Event/subscription concept and code probably does not change much
“Only” connection setup needs to be developed
IOC |  | CA Service
Connects (TCP) to well known host:port | → | Accepts connection
Sends list of PVs (necessary?) | → | Sets up monitors
Sends PV events | → | Processes data
Goes offline |  | Stops monitoring

## Slide 23: What do you think?
Does this look useful?
Channel Access or PV Access or both?
Anyone volunteering to implement it?