## Slide 1
EPICS 7
Matej Sekoranyja, Marty Karimer, Michael Davidsaver, Ralph Lange, Andrew Johnson, Timo Korhonen, Heinz Junkes, Patrick Marschalik, Murali Shankar, Bruno Martins, Kunal Shroff, Arman Arkilic, Michael Dalesio, Anton Metzger, Greg White, David Hibkin, Guobao Shen, Sinesa Veseli, Bob Dalesio, Steve Hartman

## Slide 2: EPICS 7 Outline
What is it?
Status
Services Support Application Development
Community Use
Conclusions

## Slide 3: What Is EPICS 7 (not)
V4 is not a replacement for V3
V4 does not introduce a new IOC database
V4 does not require you to rewrite all your drivers
V4 does not break existing systems

## Slide 4: What is EPICS 7
EPICS 3 is a set of tools, libraries and applications to create a distributed control system
EPICS 7 extends V3, and does not require upgrading any of your applications.
EPICS 7 adds structured data to EPICS V3

## Slide 5: EPICS 7 Improves EPICS V3
Overcome Channel Access shortcomings: Better array and string handling
Structured data: Extending the scope of EPICS from I&C to data acquisition, image processing, and beyond
Efficient network transfer: High performance archiving and image transfer
RPC type services: Service oriented architecture: archiver, snapshot, database backends
Complex control: Communicating with devices (groups of PVs on an IOC) in an always-consistent, transaction type way

## Slide 6: EPICS 7 overcomes some shortcomings in V3
Support for 64bit integers
  1/8/16/32/64bit integers, signed and unsigned
Better support for arrays
  No element_count upper limit (fixed and bounded arrays possible)
  Clear distinction between arrays of size 1 and scalars
  Axis metadata is transmitted with the array
Better support for strings
  Arbitrary size
  No fixed limit or need for long string workaround
Much better support for arrays of strings
  Handles arbitrary number of arbitrary length strings

## Slide 7: EPICS 7 Supports Structured data
V4 can do everything V3 can do (but better): Can construct pvData structures analogous to DBR types. For example the equivalent of a DBR_TIME_DOUBLE would be the structure:
NTScalar
double value
alarm_t alarm
int severity
int status
string message
time_t timeStamp
long secondsPastEpoch
int nanoseconds
int userTag

## Slide 8: EPICS 7 Provides Efficient network transfer
pvAccess operations only send deltas on the wire. So if the value of the structure in the above example is modified to:
NTScalar
double value 8.1
alarm_t alarm
int severity 2
int status 3
string message HIHI_ALARM
time_t timeStamp
long secondsPastEpoch 1460589145
int nanoseconds 588698520
int userTag 0
only changed values (in bold) need be sent, plus a bitset indicating which fields have changed value.

## Slide 9: EPICS 7 Supports RPC type services
RPC type services can use structures that are different for every call and different for put (request) and get (response). pvData can encode more complex data types like a table:
NTTable
string[] labels [value, seconds, nanoseconds, status, severity]
structure value
double[] value [ 1.1, 1.2, 2.0]
long[] secondsPastEpoch [1460589140, 1460589141, 1460589142]
int[] nanoseconds [ 164235768, 164235245, 164235256]
int[] severity [ 0, 0, 1]
int[] status [ 0, 0, 3]

## Slide 10: EPICS 7 Provides Complex control
Possible to create complex structures representing, for example, a detector, camera driver, file writer or camera plugin
Can operate on subset of fields for control or monitor whole structure
With RPC can add “methods” and create distributed objects

## Slide 11: EPICS 7 Base Status
Build System builds EPICS 3 and pvAccess into the single EPICS 7 Release
pvAccess and pvData run alongside of Channel Access and DBR_types
pvData supports structured data
NTypes are standard pvData for DBR_types, Tables, N-D Arrays, Heterogeneous Arrays, etc..
pvAccess provides improved metadata for the IOC Database
pvAccess provides communication mechanism for Relational DB and No SQL DB Services
pvAccess Gateway Alpha Release
pvAccess Database Links (2018 Q2)
Access Security (Not Yet Scheduled)
Data Aggregation is planned for Java Client API (2018 Q2)
Data Aggregation is planned for C++ Client API (Not Yet Scheduled)
EPICS Records To Take Advantage of NTYpes (Not Yet Scheduled)

## Slide 12: EPICS 7 Service Status
Standard Services are developed to demonstrate the use of these mechanisms:
IOC (QSRV) 2017, Q3
areaDetector 2017, Q1
Directory 2017, Q3
Save Sets 2017, Q3
Data Index 2017, Q3
Archive 2018, Q2
Log Book 2018, Q2
Snap Shot 2018, Q2
Alarm Not Yet Specified
Unit Tests and Performance Tests are provided with most code
Python, Matlab, C++, and Java APIs available for client and service development

## Slide 13: Standard Clients Are Developed for NTypes
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
CSStudio
Python, C++, Java
Configuration
Data Archive
Archive
E Log
NoSQL

## Slide 14: Standard Services Support Application Development
IOC
Directory
NoSQL
Instrumentation
Feedback Control
Physics Code Receives EPICS PV Names
Given Physics Device and Properties
From a Directory Service
E Log
NoSQL
Data Archive
Archive
I to Field
NoSQL

## Slide 15: Feedback Control Application Uses Standard Services – Read/Write Instrumentation
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Reads All Set points and Readbacks to Calculate Errors
Errors are used to Calculate New Field Settings for Magnets
E Log
NoSQL
Data Archive
Archive

## Slide 16: Feedback Control Application Uses Standard Services – Complex Conversions
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Sends Designed Field Setting to Conversion Service
and Receives New I Settings
E Log
NoSQL
Data Archive
Archive

## Slide 17: Feedback Control Application Uses Standard Services – Instrumentation Interfaces
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Sends New Current Setting
to Magnet Power Supply
E Log
NoSQL
Data Archive
Archive

## Slide 18: Feedback Control Application Uses Standard Services
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Records the Activity Into Official Logbook
Lists all PVs used
E Log
NoSQL
Data Archive
Archive

## Slide 19: New Services Can Be Added Easily
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Data Archive
Archive
E Log
NoSQL
Data Set
Snap Shot Data Set
HDF5
Data Index
Index Data Set
NoSQL
Alarm
NoSQL

## Slide 20: Who is using EPICS 7 at this time?
NSLS-II/FRIB/RAON: middle-layer services using structured data
  In production: Channel Finder, MASAR service for save sets, Data Index
  More services planned (archiver, snapshot data, elog, ...)
SNS Beamlines: implementing next generation of controls and data acquisition
LCLS I/LCLS II: re-implementing all high-level physics database access using pvAccess and middle-layer services
FHI: using archiver appliance with pvAccess and structured data
APS: uses v4 RPC services for large buffer transfer
Diamond/NSLS-II: transferring areaDetector images across the network / between processes using pvAccess
  Using >90% of physical bandwidth on 10Gb ethernet (no compression)

## Slide 21: Conclusions
EPICS 7: pvAccess extends V3 without replacing the existing IOC
pvData and pvAccess add flexible structures w efficient network protocol
NTypes is Set of well-defined containers for generic clients
Beyond beta status, first in-production users are happy
Developments are ongling………
EPICS 7.0 release will be ready 10/31 (if you can’t wait… contact us)