## Slide 1: Target and Dump Proton Beam Imaging Systems CDR
Thermal Heat Load Analysis
of First Mirror

## Slide 2: Introduction
Notes: Heat induced/generated from spallation products from target wheel.
There is a possibility that the generated heat load is so large that it will result in permanent damage of mirror and/or mirror mount.
In addition, deformations of mirror and/or mount can cause optical problems.
Thus: need to ensure that there is sufficient thermal connection to the cooled PBIP.

## Slide 3: Aim of the Heat Laod Analysis
Plot deflections of the first mirror and mount.
  Affect on beam path
  Note: Not looking into deformations of the PBIP
Find most optimal mount design
  Shape
  Material
Note: This is a simplified heat load analysis, to get a first indication of how mirror and mount is affected by the heat load. A more detailed analysis shall be run, including the complete PBIP.

## Slide 4: The Heat Load
Input from ESS target division
Heat load [W/cm3] around proton beam line inside the monolith vessel. Data for each point (x,y,z), the coordinate system is TCS. (March 2017)
  .
  x=0 is inside the target wheel and the x axis is pointing along the beam axis towards the proton beam window.
  Coordinates close to the mirror (150, -16, 0) and mirror mount.
We considered this area (ref. Alan Takibayev):
    153 < X < 158
    -13 < Y < -20
    -3.5 < Z < 3.5
Average heat load: 0.0216 ± 0.0017 W/cm³ = 21600 W/m3
Worst case/Max heat load approx.: 0,4 W/cm3 = 4x105 W/m3

## Slide 5: PBIP Temperature
  Doc nr. ESS-0052276 (March 2016) Thermal deformation of the PBIP
  PBIP temperature is about 60 ͦC at the surface where mirror and mount will be located.

## Slide 6: Simulation Model CAD model – Mesh – Boundary Cond.
Base Plate
(Section of the PBIP that the mount is fixed onto)
Mount
Mirror
Type of boundary condition | Value | Comment
Initial temperature of mirror and mount. | 308 K (35 ͦC) | Same boundary condition as used for PBIP thermal analysis. Doc nr. ESS-0052276 (Mar. 2016)
Base plate temperature | 333 K (60 ͦC) | This value is taken from the old analysis: Thermal deformation of the PBIP. Doc nr. ESS-0052276 (Mar. 2016)
Convection from mirror and mount, to surrounding gas/vacuum | 0,5 W/m2K | With specified ambient temp 308 K (35 ͦC)
Heat radiation emissivity for Aluminium | 0,05 | With specified ambient temp 308 K (35 ͦC)
Heat radiation emissivity for Steel | 0,1 | With specified ambient temp 308 K (35 ͦC)

## Slide 7: Simulation Model Material Properties
Material Property | Material | 
 | Al 6061 | Stainless Steel
C, Specific Heat [J/kg K] | 897 | 477
K, Thermal conductivity [W/m K] | 167 | 16,2
α, Thermal Exp. Coeff [/K] | 2,4e-5 | 1e-5
Reference Temperature [K] | 293 | 293

## Slide 8
Bonded surface contact between:
  Mount and base plate
  Mount and mirror
Base plate constraints
  Fixed constraint for all surfaces, except from the top surface.
Heat loads
  Average: 21600 W/m3
  Max: 4 x 105 W/m3
Simulation Model Loads and Constraints

## Slide 9: First simulation model Bendamount
Load case | Temperature of mirror | Figure
21600 W/m3 heat load | 426 K / 153 ͦC | 
4 x 105 W/m3 heat load | 755 K / 482 ͦC | 
Steel

## Slide 10: Simplified Mount Larger Surface Contacts
Load case | Temperature of mirror Bendamount | Temperature of mirror Simplified steel mount | Temperature of mirror Simplified aluminium mount
21600 W/m3 heat load | 426 K / 153 ͦC | 340 K / 67 ͦC | 334 K / 61 ͦC
4 x 105 W/m3 heat load | 755 K / 482 ͦC | 476 K / 203 ͦC | 353 K / 80 ͦC

## Slide 11: Simplified Mount Mirror Deflections
Load case | Max deflection Steel mount | Max deflection Aluminium mount | Max deflection SHORT steel mount
21600 W/m3 heat load | 340 K / 67 ͦC 0,859 x 10-4 m | 334 K / 61 ͦC 1,161 x 10-4 m | 334 K / 61 ͦC 0,670 x 10-4 m
4 x 105 W/m3 heat load | 476 K / 203 ͦC 3,175 x 10-4 m | 353 K / 80 ͦC 1,578 x 10-4 m | 378 K / 105 ͦC 1,567 x 10-4 m

## Slide 12: Design Change - Mirror
65 mm
75 mm

## Slide 13: Short Mount Mirror Deflections
Load case | Max deflection SHORT steel mount Original mirror | Max deflection Steel mount Large mirror
21600 W/m3 heat load | 334 K / 61 ͦC 0,670 x 10-4 m | 334 K / 61 ͦC 0,721 x 10-4 m
4 x 105 W/m3 heat load | 378 K / 105 ͦC 1,567 x 10-4 m | 380 K / 107 ͦC 1,558 x 10-4 m

## Slide 14: Short Mount Mirror Deflections
Load case | Max deflection Steel mount Large mirror | Max deflection Aluminium mount Large mirror | Max deflection Straight Steel mount Large mirror | Max deflection Straight Al. mount Large mirror
21600 W/m3 heat load | 334 K / 61 ͦC 0,721 x 10-4 m | 333 K / 60 ͦC 0,788 x 10-4 m | K / 62 ͦC 0,570 x 10-4 m | 428 K / 155 ͦC 0,815 x 10-4 m
4 x 105 W/m3 heat load | 380 K / 107 ͦC 1,558 x 10-4 m | 342 K / 69 ͦC 0,858 x 10-4 m | 428 K / 155 ͦC 2,27 x 10-4 m | 344 K / 71 ͦC 0,842 x 10-4 m

## Slide 15: Conclusion
Simplified mount design
Short mount
Angled mount design (Do not need to implement angled surface in plug)
Aluminium material
Note: These conclusions are based on PBIP reference temperature of 60 ͦC, from “Thermal deformation of the PBIP” Doc nr. ESS-0052276.

## Slide 16: Result plots Current mirror and mount design
Load case | Aluminium mount Large mirror | Figures
21600 W/m3 heat load | 333 K / 60 ͦC | 
 | 7,876 x 10-5 m | 
4 x 105 W/m3 heat load | 342 K / 69 ͦC | 
 | 8,582 x 10-5 m | 

## Slide 17: Result plots
In order to study the optical effects of the thermal deformations,
the deformations in the worst case heat load have been used.

## Slide 18: Further Work
Final mount design
  Shape
  Assembling method
  Interface towards PBIP
Final, more detalied thermal analysis, including PBIP.