## Slide 1: Assembly Instruction Bunker Wall Blocks ESS-0191778 Preliminary TBD with supplier
Thorbjörn Lindwall
Design engineer
www.europeanspallationsource.se
4 December, 2017

## Slide 2
Walls Blocks
Summary
The bunker walls are made up from
50mm layers of HDPE and Steel
The different blocks are hold together
Using 50 or 60mm steel rods.
The rods are welded to the outer
steel layers of the blocks.
HDPE shown in red.
Steel shown in grey.
Typical wall block ( R28 L2)

## Slide 3
Walls Blocks
Wall blocks
The blocks have different
layout of steel and HDPE
depending were the block are placed.
All blocks have a Three
reference surfaces
Typical wall block ( R28 L2)
Reference surface

## Slide 4
Walls Blocks
Assembly order
Start with stacking steel layers in block 1.
(Fixture TBD with supplier)
Add block 3-5 (number of steel/HDPE differ
depending of which type of wall block it is)
Insert the steel rods
Weld the steel rods to the outer steel layers
(weld method TBD with supplier)
Weld the adjacent steel layers together using
3x 100mm butt welds on each side.
Typical wall block ( R28 L2)
6.
5.
4.
3.
2.
1.
Weld
Welds