## Slide 1: Feed through neutronics calculation Valentina Santoro on behalf of the neutronics bunker team G. Muhrer, D. Di Julio, S. Ansell, E. Klinkby

## Slide 2
Utilities feed through (I)
Detailed simulation in mcnp6 of the engineering model
The utilities feed-through are located on top of the beam line

## Slide 3
Utilities feed throughs(II)
Engineering Model
MCNP6 Model
Detailed simulation in mcnp6 of the engineering model
Feed through neutronics calculation

## Slide 4
Assumptions
We computed the feed-through radiations using the worst
possible case scenario for spreading the radiation throughout
the bunker roof
This scenario is represented by a straight focusing metallic
guide
Guide ends before the bunker wall at 11.5 m with a width and height of
1 cm (aluminum substrate )
Guide in the bunker starts at 6m with a width and height of 10 cm (aluminum substrate)

## Slide 5
Radiation Dose Map in the bunker
Al Guide
Monolith
Bunker Wall
Entrance of Feed-throught
~ 58mSv/h
Bunker Roof
mSv/h
Feed through neutronics calculation

## Slide 6
Radiation Dose Map in the feed-through
Al Guide
mSv/h
Bunker Wall
Feed-through
Exit of Feed-through ~ 10mSv/h
NEUTRONS
Feed through neutronics calculation

## Slide 7
Al Guide
mSv/h
Bunker Wall
Radiation Dose Map in the feed-through
PHOTONS
Feed through neutronics calculation
Exit of Feed-through << 1mSv/h

## Slide 8
Status of the neutronics calculation after PDR
the radiation escaping the feed-through are around 10-15 mSv/h
to achieve the safety limit of 3 mSv/h (1.5 mSv/h in Monte Carlo simulation) we need to fill the feed-through
from neutronic point of view we need to simulate a sufficient filling fraction to reduce the amount of the radiation
Feed through neutronics calculation
Note: these numbers have been verified with hand calculation (see
ESS-0118440)

## Slide 9
Radiation Dose Map in the feed-through
Al Guide
Bunker Wall
Feed-through
Exit of Feed-through << 1mSv/h
50% filling fraction
Feed through neutronics calculation
mSv/h
Imp =0 for guide in the bunker wall

## Slide 10
Radiation Dose Map in the feed-through
Al Guide
mSv/h
Bunker Wall
Feed-through
Exit of Feed-through < 1 mSv/h
30% filling fraction
Feed through neutronics calculation
Imp =0 for guide in the bunker wall

## Slide 11
Summary
Neutronics calculation for the utilities feed-through have been performed
The feed-through design is viable
A filling fraction of 30% is enough to bring the radiation to the required safety limit for a standard ESS-beam line
Feed through neutronics calculation
For additional information ESS-0118440

## Slide 12
BACK-UP SLIDES

## Slide 13
Bunker feed throught HAND CALCULATION
H0
H1
H2
H3
H4
H5
L1

## Slide 14
Assumptions (II)
Source term at the 2m position
LOKI BEAM LINE N7

## Slide 15
Source term

## Slide 16
Al Guide
mSv/h
Bunker Wall
Feed-through
Exit of Feed-through ~ 10mSv/h

## Slide 17
Al Guide
Bunker Wall
Exit of Feed-through << 1mSv/h
mSv/h

## Slide 18
Al Guide
Bunker Wall
Feed-through
Exit of Feed-through << 1mSv/h
Imp =0 for guide in the bunker wall
mSv/h

## Slide 19
Al Guide
mSv/h
Bunker Wall
Feed-through
Exit of Feed-through < 1 mSv/h
Imp =0 for guide in the bunker wall