## Slide 1: BUNKER SYSTEM DOCUMENTATION Critical Design Review (CDR) 5 December 2017
Mark Ridgley
Technical Documentation Coordinator
Bunker Project
europeanspallationsource.se

## Slide 2: Bunker System Life-cycle ConOps ESS-0123251
FINAL ENGINEERING DESIGN
PRELIMINARY ENGINEERING DESIGN
CONSTRUCTION & INSTALLATION
BEAM TEST & COMMISSIONING
GENERAL OPERATIONS
PLUS MAINTENANCE, UPGRADES & DEVELOPMENT
DESIGN
CONSTRUCTION
OPERATIONS
DECOMMISSIONING
DECOMMISSIONING & DISPOSAL
2065
TBD
2023
2019
2016
2013
KICK-OFF
SAR
ORR
PDR
FIRST BEAM ON TARGET
HANDOVER
Preliminary Engineering Design | Final Engineering Design | Construction & Installation | Beam Test & Commissioning | General Operations | Decommissioning & Disposal
Purpose: Develop ConOps and draft SyR for desired solution from a broad spectrum of ideas and alternatives. Determine feasibility of desired system and identify potential technology needs. Define the selected solution in enough detail to establish an initial baseline capable of meeting user needs. Develop system structure end-product requirements and generate a preliminary design with documentation. | Purpose: Finalize design and generate final designs for each system end-product. Develop the engineering documentation for procurement of materials and of manufacturing. | Purpose: Procure materials and manufacturing of system end-products. Develop SIPr prior to installation and SVePr for post installation. Develop as-manufactured engineering documentation for manufacturing procurement. Assemble and integrate system end-products to meet requirements and document in SIR. Prepare transition to operations. Conduct system verification and document in SVeR. Develop as-built 3D engineering models. Develop SVaPr to prepare for system validation. | Purpose: Completion of the system integration and system validation i.a.w. SVaPr with results documented in SVaR. Finalization of the as-built 3D engineering models, SDD and SOMM. Closure of Bunker Project and handover of the Bunker System to ESS Facility Operations. | Purpose: Conduct normal operations as part of the ESS Facility Operations and meet the initially identified need and maintain support for that need as per SOMM. Training of operators and maintainers. Train replacement operators and maintainers. Maintain and approve operations and maintenance logs. Maintain and upgrade of system. | Purpose: The decommissioning, disassembly and disposal of the system i.a.w. SDDPr. Provide SCR and include the documenting of lessons learnt.
Output: Preliminary design definition in the form of simulations, analysis and 3D engineering models. Concept of Operations (ConOps). System Requirements Specification (SRS). System Architecture Description (SAD). System Validation Plan (SVaP). System Integration Plan (SIP). System Verification Plan (SVeP). | Output: Final design definition in the form of simulations, analysis and 3D engineering models. Final ConOps, SRS, SAD. Final SVaP, SIP, SVeP. System Operation and Maintenance Manual (SOMM). Systems Design Description (SDD). Safety Analysis Report. Structural Verification Status Report. Engineering documentation for manufacturing procurement. | Output: System Integration Procedure (SIPr). System Verification Procedure (SVePr). System Integration Report (SIR) System Verification Report (SVeR). System Validation Procedure (SVaPr). As-manufactured engineering documentation. As-built 3D engineering models. | Output: System Validation Report (SVaR). Final SOMM, SDD. Final as-built 3D engineering models. | Output: Operations logs Maintenance logs | Output: System Decommissioning and Disposal Plan (SDDP). System Decommissioning and Disposal Procedure (SDDPr). System Closeout Report (SCR).
CDR
2017

## Slide 3: Bunker Project Documentation Delivered for CDR
Final design definition in the form of:
  Neutronics simulations and analysis
  3D engineering models
  Engineering simulations and analysis
Engineering documentation for manufacturing procurement
Systems Documentation
  Concept of Operations (ConOps)
  System Requirements Specification (SRS)
  System Architecture Descriptions (SAD)
  Systems Design Description (SDD)
  System Integration Plan (SIP)
  System Verification Plan (SVeP)
  System Validation Plan (SVaP)
  System Operation and Maintenance Manual (SOMM)
  System Interface Description (SID)

## Slide 4: Bunker System Documentation w.r.t. PSAR and SSM
Preliminary Safety Assessment (PSAR) as presented to Swedish Radiation Safety Authority (SSM)
  Section 3.2. Radiation Safety Analyses & Methodologies
    Illustration of ESS design process as defined in the system engineering management plan
Notes: Radiation safety analyses and methodologies are an integral part of ESS’s design methodology.
Radiation safety management is a sub-set of risk management activities performed at ESS.
The ESS design process starts by identifying the stakeholder needs and the operational context for the facility. From these, requirements for the facility are derived and required functions are defined. The facility is decomposed into system elements, based on use cases and functional analysis, and requirements are allocated to each system element. This process is then repeated for each system element in an iterative and recursive fashion, as illustrated in Figure 3-1, until a level of detail has been reached where detailed design and system realisation can occur.
The specific instance of a system or sub-system is referred to as the system of interest.

## Slide 5: ESS Facility Breakdown Structure CHESS
=ESS.NSS.F01.F01
Shielding & Safety System
Bunker System

## Slide 6: Bunker System Documentation ESS-0123251 - Concept of Operations (ConOps)
Primary purpose - provide a shared cavity shielding bunker at the target monolith to:
  Host Instrument Systems front-end elements.
  Attenuate the radiation emanating from the target monolith and generated in the first sections of the beam-lines (neutron and gamma rays) to safe levels external to the bunker.
Bunker System ConOps Scope:

## Slide 7: Bunker System Documentation ESS-0060210 - System Requirements Specification (SRS)
SRS specifies and describes the system requirements for the Bunker System (BS.SyR).
Derived from:
  high-level requirements allocated by the parent system - Shielding & Safety System
  ConOps for the Bunker System
  feedback from the evolving design development of the system
BS.SyR are defined according to the different categories and each is uniquely identified:
  Functional Requirements
  Constraint Requirements
  Seismic Safety Requirements
  Radiation Safety Requirements
  Interface Requirements
BS.SyR are applied to the requirements driven development of the system design.
Notes: Bunker System Requirements will be presented in separate presentation.

## Slide 8: Bunker System Documentation ESS-0123443 - System Architecture Description (SAD)
SAD describes the system architecture and allocation of BS.SyR to subsystems.
BS.SyR are allocated to at least one subsystem.
Bunker System Breakdown Structure
(simplistic)
Notes: Logical system breakdown effectively describes the different functions that the specialized subsystems provide.
Note that the concrete base slabs that constitute the bunker base in D building D01 (Experimental Hall 1), D building D03 (Experimental Hall 2) and the Monolith Civil Structure (MCS) of D building D02 (Target Building) are not part of the Bunker System. They are part of Site Infrastructure (SI).

## Slide 9: Bunker Subsystem Documentation ESS-0123282 - ConOps for the Bunker Structural Support System
System purpose of the Bunker Structural Support System is to:
  provide the load paths through to the bunker base of the Monolith Civil Structure (MCS) in D-Building D02 (Target Building) and the bunker base in D01 (Experimental Hall 1) and D03 (Experimental Hall 2) to resist dead load, live loads and accidental loads.
  provide structural support for the bunker roofs.
  provide interfaces for the routing of required utilities within the bunker.
  provide the structure that ensures Bunker System requirements at H4 seismic event are fulfilled.
  allow for the allocation of reserved volume for each Instrument System (IS) along its designated beam-port central axis from the target to the bunker walls for its front-end system elements installed within the bunker.
Notes: In doing so this system contributes to the fulfilment of the system purpose of the Bunker System which is to host Instrument Systems elements and associated equipment and attenuate the radiation emanating from the target monolith and generated in the first sections of the beam-lines (neutron and gamma rays) to safe levels external to the bunker.

## Slide 10: Bunker Subsystem Documentation ESS-0123283 - ConOps for the Bunker Wall System
System purpose of the Bunker Wall System is to:
  provide attenuation of radiation emanating outwards from within the bunker down to safe levels external to the bunker.
  ensure attenuation of radiation emanating from within the bunker through where the base of the bunker walls interface with the bunker base respectively in the Monolith Civil Structure (MCS) of D-Building D02 (Target Building), in D-Building D01 (Experimental Hall 1) and D-Building D03 (Experimental Hall 2) down to safe levels external to the bunker.
  modular in form to provide safe feed-through of Instrument Systems (IS) elements (e.g. instrument guides) from within the bunker into D01 and D03 respectively.
  modular in form to allow modification to suit installation or removal of IS elements (e.g. instrument guide).
  modular in form to provide safe feed-through routing of utilities into the bunker from D01 and D03 for IS elements within the bunker.
  impede access to the bunker.
  modular in form to provide restricted secondary access for the passage of large IS elements for installation or removal when access passage through the bunker roof is not sufficient.
Notes: In doing so this system contributes to the fulfilment of the system purpose of the Bunker System which is to host Instrument Systems elements and associated equipment and attenuate the radiation emanating from the target monolith and generated in the first sections of the beam-lines (neutron and gamma rays) to safe levels external to the bunker.

## Slide 11: Bunker Subsystem Documentation ESS-0123286 - ConOps for the Bunker Roof System
System purpose of the Bunker Roof System is to:
  provide attenuation of radiation emanating upwards from within the bunker down to safe levels external to the bunker.
  modular in form to provide restricted personnel access to the bunker.
  modular in form to provide primary access for the passage of Instrument Systems elements, Target Systems elements and associated equipment for installation or removal.
Notes: In doing so this system contributes to the fulfilment of the system purpose of the Bunker System which is to host Instrument Systems elements and associated equipment and attenuate the radiation emanating from the target monolith and generated in the first sections of the beam-lines (neutron and gamma rays) to safe levels external to the bunker.

## Slide 12: Bunker Subsystem Documentation ESS-0123281 - ConOps for the Bunker Access Safety System
System purpose of the Bunker Access Safety System is to:
  provide safe restricted authorised personnel access to the bunker roofs.
  provide safe restricted authorised access into the bunker.
Notes: In doing so this system contributes to the fulfilment of the system purpose of the Bunker System which is to host Instrument Systems elements and associated equipment and attenuate the radiation emanating from the target monolith and generated in the first sections of the beam-lines (neutron and gamma rays) to safe levels external to the bunker.

## Slide 13: Bunker System Documentation System and Subsystems
Refer to:
BunkerSystem-doc.tif

## Slide 14: Bunker System Documentation ESS-0087572 - System Interface Description (SID)
SID captures and describes project specific interface agreements with neighbouring systems; Site Infrastructure, Target Systems and Instrument Systems:
  ESS-0062997, Bunker shielding roof seismic load on MCS
  ESS-0085422, Boundary interfaces definition; Bunker – CF
  ESS-0068165, Bunker layout – Interfaces – static load
  ESS-0084435, Bunker pillar loads calculation
  ESS-0086197, Bunker to the insert exchange tool interface
  ESS-0051975, Bunker base support pillars
  ESS-0062215, Feed-thru block assembly
  ESS-0062127, Short instrument wall feed-thru outline
  ESS-0062152, Long instrument wall feed-thru
  ESS-0086538, Utilities feed-through layout
  ESS-0086925, Bunker to Target interfaces
  ESS-0049906, ICD-R NBEX-NSS
The agreed to interface solutions at preliminary design stage and used as input into the final design engineering.
Notes: Not an interface control document.
Used as input into the design engineering only.
The end design output is described in the System Design Description (SDD).

## Slide 15: Bunker System Documentation ESS-0123264 - System Design Description (SDD)
SDD provides the documented description of the design of the Bunker System that is to be built.
SDD is comprised of the SDDs of its subsystems.
SDD captures for subsystems and complete system:
  Design engineering
    3d models.
    Simulations & analysis.
    Engineering drawings for manufacture procurement.
  Neutronics
    Simulations & analysis.

## Slide 16: Bunker System Documentation ESS-0123264 - System Design Description (SDD)
Bunker System
Product Breakdown

## Slide 17: Bunker System Documentation ESS-0123264 - System Design Description (SDD)
Bunker Structural Support System
Product Breakdown
ESS-0123449 SDD

## Slide 18: Bunker System Documentation ESS-0123264 - System Design Description (SDD)
Bunker Wall System
Product Breakdown
ESS-0123450 SDD

## Slide 19: Bunker System Documentation ESS-0123264 - System Design Description (SDD)
Bunker Roof System
Product Breakdown
ESS-0123452 SDD

## Slide 20: Bunker System Documentation ESS-0123264 - System Design Description (SDD)
Bunker Access Safety System
Product Breakdown
ESS-0123448 SDD

## Slide 21: Bunker System Documentation ESS-0123956 - System Integration Plan (SIP)
SIP provides the documented description of the plan for integration of the Bunker System into the ESS facility.
SIP is comprised of the SIPs of its subsystems.
Subsystem SIPs developed from respective subsystem SDD.
Captures the design engineers’ plan that is the input provided to the project installation plan.
System Verification and Validation are generally carried out as the system integration progresses and close out at its completion.

## Slide 22: Bunker System Documentation ESS-0123956 - System Integration Plan (SIP)
Bunker System Integration

## Slide 23: Bunker System Documentation System Integration, Verification and Validation
Roof NW & SE ESS-0147794
Wall NW ESS-0147791
Structural Support NW ESS-0147784
Structural Support SE ESS-0147784
Walls SE ESS-0147791
Preparation & planning
Verification ESS-0123957
Validation ESS-0123947
Handover
Access Safety NW & SE ESS-0147794
Refer to:
BunkerSystem-integration.tif
Notes: High-level (simplistic) integration plan of the Bunker System.
System Integration Plan (SIP) ESS-0123956.
System Verification Plan (SVeP) ESS-0123957.
System Validation Plan (SVaP) ESS-0123947.

## Slide 24: Bunker System Documentation ESS-0123957 - System Verification Plan (SVeP)
TBA
TBA

## Slide 25: Bunker System Documentation ESS-0123947 - System Validation Plan (SVaP)
TBA

## Slide 26: Bunker System Documentation ESS-0124440 - System Operations & Maintenance Manual (SOMM)
TBA