## Slide 1
Current Status of J-PARC MLF
Toshiji Kanaya
J-PARC, MLF KEK
ESS – J-PARC Workshop
Lund, 18, 19 January 2018

## Slide 2
LINAC
400 MeV
Rapid Cycle Synchrotron
3 GeV, 25 Hz
Main Ring
50 GeV
Neutrio Experimental Facility
Hadron Experimental Facilty
Material & Life Science Experimental Facility (MLF)
Notes: まず、こちらが、J-PARCの加速器複合施設です。陽子ビームを１８１MeVまで加速する（来年度以降４００ MeVになる）線形加速器ライナックがあり、その後、ビームは、40 msという短い時間の間に3 GeVまで加速されます。そのビームのほとんどは、この物質生命科学実験施設で中性子やミュオンを使った実験の為に使われています。

## Slide 3
W
W/O
W
W/O
Higher freq. components, related with cavitation phenomena, were sufficiently mitigated.
Proton
High power operation (1MW)
Stable operation
Notes: This is result.
The beam power is 300 kW.
Due to the bubble injection, the velocity of vessel wall dramatically reduced and the high frequency components also almost disappeared. The high frequency components are considered to be induced by the cavitation bubble collapsing.
So that, this means the cavitation inception is mitigated.

## Slide 4
Earthquake
300 kW
Accident at
Hadron Facility
as of June 28, 2017
～10 months interruption
due to the earthquake
1 MW eq. pulse
～1 month interruption
due to the fire in MLF
Beam Power History at MLF
(before the summer shutdown in 2017)
Interruption due to troubles of Hg-target
(cooling water leakage)
500 kW
Just before the summer shutdown
Operation of target #2

## Slide 5
Replacement of target (#2) to new one (#8)
10/2：exchange work in hot cell
9/22：transfer of new target (#8) to MLF
New target (#8) in hot cell
Storage container
Storage container
Target #8
Target trolley

## Slide 6: Characteristic Features in New Target (#8)
Target #8
Region A
Region A
Region B
Region B
Bolts
Mercury vessel
Monolithic structure（Region A &B)
cut out from stainless steel block
Reduction of welding parts
Swirl bubbler
Proton
Hg
Double walled
Region A
Region B
We employed
the double wall structure to make fast mercury flow in narrow channel
He gas bubbling system
   effect was confirmed using laser doppler system
Mitigation of pitting damage
Robust structure

## Slide 7
Chart: 
Operation history of target (#8)at MLF
Operation of new target (#8) started from Oct. 24th at a power of 300 kW
Scheduled operation of 120.5 days ended in Dec. 22, 2017 with a high efficiency of 92%.
Beam delivery resumed from Jan. 10th at 400 kW.
Beam Power (kW)
Operation Efficiency (%)
2017
Winter outage
(from Dec. 23 to Jan. 8)
Daily operation
efficiency
As of January 14, 2018
2018

## Slide 8
Hg vessel
1050 mm
Water shroud
Bolts
1st～7th (previous)
8th(current)
10th or later
R&D for further target design upgrade
Many welds incl. diffusion bonding with constraints between vessels
Monolithic structure of water shroud & Hg vessel
Monolithic structure of water shroud
Much fewer welds with constraints
Few welds with no constraints
8th
  Increasing structural robustness and keeping stable beam operation are the first priority.
Constraint-free type
  Further R&D for the fabrication technique to keep the helium layer of 3 mm gap is needed.
Constraint-free
Final goal for high power operation
Improved structure
Failed at 500kW operation
Helium layer

## Slide 9
Bubbler
Jet flow Nozzle
Under development
Countermeasure for the pitting damage
Double wall
Bubbler
Proton
Beam
mercury
No protection for damage
Schedule to 1MW
mercury
mercury
Proton
Beam
Proton
Beam
Double wall
#10 (gradually increase from 500kW to 1MW)
Depending on the results of PIE on #8, a possibility of 500 kW operation
JFY 2016 | JFY 2017 | JFY 2018 | JFY 2019 | JFY 2020
0
100
200
300
400
500
600
700
800
900
1000
MLF beam power、kW
#2 (200kW)
#2 (150kW)
#8
400 kW from January
500 kW from April
1MW test at end of June
1MW test
Operation

## Slide 10: Neutron Instruments at MLF
HRC
BL12
4SEASONS
BL01
↓
AMATERAS
BL14
↓
Experimental Hall No. 1
Experimental
Hall No. 2
DNA
BL02
↓
POLANO
BL23
VIN ROSE
BL06
S-HRPD
BL08
SPICA
BL09
TAIKAN
BL15
SOFIA
BL16
iMATERIA
BL20
NOVA
BL21
SHARAKU
BL17
RADEN
BL22
PLANET
BL11
NOBORU
BL10
NOP
BL05
ANNRI
BL04
iBIX
BL03
TAKUMI
BL19
SENJU
BL18

## Slide 11
23 Neutron Beam Ports
Operation: 20
Commissioning: 1
Yearly Operation Days
・~180
Yearly Guest Number
・800~900
4SEASONS
(JAEA)
HRC (KEK)
ANNRI
(Tokyo Tech. U., JAEA,,
Hokkaido U.)
SHRPD(KEK)
NOBORU (JAEA)
SOFIA (KEK)
iBIX
(Ibraki Pref.)
iMATERIA
(Ibraki Pref..)
TAKUMI (JAEA)
NOVA
(NEDO, KEK)
AMATERAS
(JAEA)
PLANET (JAEA, U. of Tokyo)
DNA (JAEA)
SENJU (JAEA)
SHARAKU
(JAEA)
SPICA
(NEDO, KEK)
Funded
Funded
Funded
Funded
Funded
Funded
Operation
Operation
Operation
Operation
Operation
Operation
Operation
Operation
Operation
NOP(KEK)
Operation
Operation
Operation
Operation
Operation
Operation
Operation
VIN_ROSE
(KEK, Kyoto Univ.)
RADEN
(JAEA)
POLANO
(Tohoku Univ,, KEK)
commissioning
Neutron Instruments at MLF
Operation
Operation
Operation
TAIKAN
(JAEA)
Operation
Notes: この核破砕中性子源を利用するMLFには，23の中性子を取り出すビームポートがあり，それらに，基礎物理から化学，生命科学，材料，機械工業まで多岐にわたる実験課題を遂行するための様々な実験装置が設置される予定です．最終的には，年間約1万人日が利用し，年間でおよそ2000件程度の実験課題を実行していくことになると予想されています．
現在は，そのうち14台の実験装置の設置計画が進行しており，KEK4台，茨城県が2台，その他大学等のグループから4台，そして，原研では，残留応力解析用パルス中性子回折装置，生物用非弾性散乱装置DIANA，大強度型小角散乱装置，汎用粉末回折計，生物用単結晶回折計，そして，冷中性子ダブルチョッパー型分光器の6台の設置計画を進めております．
本日は，この私が担当しております冷中性子ダブルチョッパー型分光器についてお話しさせていただきます．

## Slide 12: Spectroscopy Group 6 Inelastic Scattering Instruments covering a wide energy and momentum transfer range
BL01(4SEASONS)
(JAEA)
BL02 (DNA)
(JAEA)
BL06(VIN_ROSE)
(KEK, Kyoto Univ.)
BL14 (AMATERAS)
(JAEA)
BL23 (POLANO)
(Tohoku Univ., KEK)
Figure 2 Covered E-Q space of inelastic neutron scattering instruments in MLF.
Spin Echo
BL12 (HRC) (KEK)
R. Kajimoto, T. Yokoo
Notes: We also have some inelastic scattering machines with various energy resolutions.
DNA on BL02 is a backscatterig machine with energy resolution of ~3ueV, AMATERAS on BL14 is a low energy inelastic machines below about 100 meV. 4SEASON can cover several to several hundred meV region.
Spin-Echo machine is under construction, which will cover neV region.
Using these inelastic scattering machines, we can cover a very wide energy region from ueV to 1000 meV

## Slide 13: Crystal Structure Group 7 Diffraction Instruments at MLF
Diffractometer in the World
SHRPD
Ibaraki Powder Diff.
Versatile Total Scattering Diff.
・lowest gauge：1 mm3
・2×2×2mm3, 30mm path in Fe：～3 min
・stress resolution：～±15MPa（Steel）
TAKUMI: Engineering Materials Diff.
Ibaraki Biomaterial Single-Xtal Diff.
・50 x BIX-3@JRR-3
・dmax ~ 135 Å
SPICA
(BL09, KEK)
Special sample environment
S. Harjo, M. Yonemura
BL18, SENJU
Single Crystal Neutron Diffractometer
Notes: Bases on the time-of-flight technique, we have developed many neutron scattering machines. They can be classified into several groups.
One is a group of diffraction machines with various resolution and intensity.
Super HRD has a very high resolution of 0.03%, which is the highest in the world.
On the other hand, NOVA has a very high intensity, but the resolution is not so good..
IBARKI power diffraction machine is in between
iBIX is dedicated to the biomaterial single crystal diffraction.
And TAKUMI is engineering materials diffraction machine,

## Slide 14
BL15 TAIKAN
(SANS)
BL16 SOFIA
(horizontal NR)
BL17
(Vertical NR)
Polarized Neutron
small - angle bank
(Semi Macro strct)
Middle
(intermid strct)
High (atomic strct)
backward
Absolute intensity data of Glassy Carbon calibrated by Dr. Ilavsky (APS)
Glassy Carbon
Nano Structure Group
1 SANS Machine, 2 Refrectmeters and 1 total scattering
Diffractometer for Nano structure and surface/interface structure
BL21 Versatile Total Scattering Diff. （NOVA)
K. Suzuya, N. Yamada
Notes: We also have SANS machine and reflectometers to investigate nanostructure and the surface/interface structure.
TAIKAN on BL15 is SANS machine and can cover a very wide Q range in one measurement. This is a great advantage of pulse neutron.
Refelectometer is also suitable machine to pulse neutron. Using our neutron reflectometer, we can cover a very wide dynamic range over 7 decades.

## Slide 15
Pulsed Neutron Application Group
Neutron Source Diagnostic & Test Port
BL10: NOBORU
Neutron-Nucleus Reaction Meas. Inst.
BL04: ANNRI
Fundamental Physics
BL05: NOP
Neutron Imaging
BL22: RADEN
K. Oikawa, T. Ino

## Slide 16
Chart: Approved/Reserved/Not approved/Conducted proposals(#)
| 2008 | 2009A | 2009B | 2010A | 2010B | 2011A | 2011B | 2012A | 2012B | 2013A | 2013B | 2014A | 2014B | 2015A | 2016A | 2016B | 2017A | 2017B | 2018A
Available BT(Initial) | 32 | 44 | 40 | 50 | 60 | 88 | 44 | 88 | 97 | 96.5 | 38.5 | 85 | 80 | 83 | 42 | 42 | 88 | 88
Instruments | 5 | 8 | 9 | 9 | 11 | 12 | 16 | 18 | 18 | 18 | 19 | 19 | 19 | 20 | 20 | 20 | 22 | 22
Approved | 20 | 64 | 45 | 62 | 69 | 95 | 46 | 124 | 174 | 164 | 82 | 187 | 190 | 199 | 107 | 105 | 179 | 202 | 287
Reserved | 0 | 0 | 0 | 0 | 0 | 34 | 12 | 20 | 41 | 29 | 57 | 50 | 52 | 45 | 192 | 157 | 72 | 124
Not Approved | 11 | 12 | 4 | 20 | 21 | 0 | 1 | 6 | 33 | 30 | 135 | 86 | 97 | 79 | 17 | 9 | 12 | 26
Conducted | 15 | 36 | 39 | 54 | 49 | 0 | 25 | 124 | 189 | 64 | 78 | 229 | 159 | 183 | 131 | 109
General Proposals to MLF
HFIR
SNS
Total Applied Proposals(2018A) MLF: 287 SNS: 480 HFIR: 251 (2014B)
Successful ratio: ～50% in every facilities
Benchmarking against world’s neutron facilities
Number of General Proposals
Number of General Proposals
Earthquake and Restoration Work
Hadron Incident
Target Problem
287 proposals@2018A

## Slide 17
17
Number of approved proposals:1,596(Except IMT&Pj use)
Classification of Approved Proposals in 2008-2016A
Industrial use is much as about 30% in J-PARC/MLF
Overseas
9.6%
Institute
8.0%
University
38.6%
Industry
29.4%
JAEA
１２.０％
KEK：２.４％

## Slide 18
Activities in MLF (1)
The 9th AONSA Neutron School and The 2nd Neutron and Muon School will be Jointly organized in Japan.
time: November 16 -20, 2017
Place: J-PARC MLF
Principal: professor Y. Kiyanagi (president of JSNS)
Number of participants: 49 from 13 countries
    Japan(9), Korea(10), India(5), Australia(5), Thailand(5), China(4), Indonesia(4), Malaysia(2), Nepal(1), New Zealand(1), Russia(1), Taiwan(1), Vietnam(1)

## Slide 19: Improving MLF to produce high quality scientific outcomes
12 press release in 2016
12 press release in 2017
論文数の推移
Chart: Publication year
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Paper | 10 | 13 | 18 | 31 | 43 | 54 | 56 | 69 | 86 | 38
Top10% proportion | 0 | 0.035088 | 0.13043 | 0.086207 | 0.06383 | 0.082192 | 0.051282 | 0.075758
Publications

## Slide 20: Science and Technology in MLF
Magnetism and strongly correlated materials(Spin ,S=1/2)
Electric properties research Gr. (K. Nakajima)
    Quantum properties research Gr. (S. Ito)
Liquid and Soft Matter (distinguish H&D)
    Polymer research Gr. (T. Kanaya)
    Soft material research Gr. (H. Seto)
    Liquid and Amorphous Materials Research Gr. (Y. Kawakita)
Energy Material (sensitive to light elements)
    Hydrogen absorbing material research Gr. (T. Otomo)
    Structure science (battery) Gr. (T. Kamiyama)
Engineering Material (deep penetration into metals)
    Residual stress research Gr. (K. Aizawa)
    Structure sensitive material research Gr. (J. Suzuki)
Muon Science
    Muon property research Gr. (R. Kadono)
    Muon science research Gr. (Y. Miyake)
Neutron Optics
KENS-DAQ
Life Science
High pressure science
Industrial Application
Characteristic features of neutron and muon
Notes: If I have time to spare at the end of my presentation, I will show you the activities of science areas based on the science groups.

## Slide 21
Sensors, Tags
mobile
PC
camcorder
Electric tools
robot
scooter
Sustainable society
Infrastructure for safety life
Research & Development Initiative of New Generation Batteries
Aiming at understanding fundamental of chemical process in battery reaction and producing new generation batteries.
(Researches are done not only in MLF, but also in other facilities)
Energy storage
Data backup in time of disaster
electric vehicle
SPICA (BL09) is a dedicated machine to the project
Energy Materials
NEDO RISING Project organized by Professor Ogumi
Professor Matsubara
Notes: I also want to mention about a big project on battery. It is organized by Professor Ogumi.
In the project, The are aiming at understanding fundamental of chemical process in battery reaction and producing new generation batteries.
For this project MLF has constructed SPICA on BL08, and many excellent results were obtained.

## Slide 22: Real-time observations of lithium battery reactions
wide
coexistent
area
In operando
measurement
SPICA (BL09) is a dedicated machine to the NEDO project for battery research
Real-time observations of lithium battery reactions—operando neutron diffraction analysis during practical operation (BL09)
Scientific Reports 6, Article number: 28843 (2016)
Special sample environment
SPICA (BL09)
Notes: They performed in operand studies on lithium ion batteries using SPICA during the discharging process.
They observed obvious difference in structure changes of anodes between 22 hrs and 2.2 hrs of discharge rates.
From this experiment we can understand the fundamental chemical process in battery reaction.

## Slide 23
Current theoretical limit
Photo-Voltaic (PV) Cell
Solar cell
Silicon
III-V semiconductors
Gallium Arsenide
Organic system
Dye-sensitized PV
Established technology
Rapid grow-up
Solar spectrum
Solar flux
(photons per unit area per unit time)
organic-inorganic hybrid perovskite semiconductors
as candidate of next generation
Photon  Electricity
In 1839, experimenting with metal electrodes and electrolyte, French physicist Alexandre Edmond Becquerel observed light-electricity conversion.
Notes: Last topic is Photo-Voltaic cell which is device for energy convergence from solar light to electricity. As you know silicon is everywhere most popular in our life. Gallium Arsenide has highest energy convergence rate. However in these several years, organic-inorganic hybrid perovskite materials are rapidly focused as candidate of next generation of PV.

## Slide 24
Bing Li et al., Nat. Commun. 8, 16086 (2017)
TO: tranverse
optical phonon
Peculiar rotation of organic molecules
causes vanishment of vibration of inorganic framework,
5K
185K
TO mode of
inorganic
framework
vanishes!
CH3NH3PbI3
inelastic neutron scattering
at AMATERAS, J-PARC
Very low heat dissipation!!
ele. dipole
4-fold rotation
3-fold rotation
organic molecule
（CH3NH3）
inorganic frame
（PbI3）
Materials | Carrier Mobility | Carrier Lifetimes | Thermal conductivity
Ideal PV’s | Large | Long | Low
CH3NH3PbI3 | Small | Very long | Low
Silicon | Large | Medium | High
> 20%
???
Atomic dynamics
electron system
atomic system
Organic-inorganic hybrid provskite semiconductor
perspective to next generation solar cell
negative electrode(Au)
positive electrode
(FTO transparent film)
heat dissipation
diffusion
photon
hole
electron
(carrier)
Three factors determining the solar cell efficiency
Notes: Typical material is methyl-ammonium-lead-iodide. Lead-triiodide forms inorganic framework and metyl-ammonium ion locates in B site of this perovskite. Characteristic properties are very long lifetime of carrier and low thermal conductivity. Mobility is small compared with silicon. As you know, perovskite is structure easily replacing ions and molecules in this case. If we obtain an ideal valance among these three factors by replacing elements and molecules, we can probably achieve much higher convergence rate. So we have to know how electronic and atomic systems collaborate.
Even at relatively low temperature, C3 rotational motions of methyl part and ammonia part individually are activated. and at high temperature phase from 165K, C4 rotation mode by which the entire molecule is rotated is activated. C-N bonding has electrical dipole, therefore C4 motion make dipole rotation. We found that optical phonon of inorganic framework vanishes by C4 rotation mode, which causes very low thermal conductivity.

## Slide 25: Development of all-solid ceramic buttery based on new super ionic conductor
Li2MCl4
Li7La3Zr2O12
LI3.3PO3.9N0.17
β-alumina
(NaAl11O17)
Single crystal β-alumina
(NaAl11O17)
Polymer Conductor
First Generation Material Family
Second Generation Material Family
LGPS-family
Organic solvent electrolyte
Li9.6P3S12
Li9.54Si1.74P1.44S11.7Cl0.3
2020
New Generation Material Family
Log [Ion conductivity (S/cm)]
Super Ionic Conductor discovered in 2016
Super Ionic Conductor discovered in 2011
Li10GeP2S12
Nature Materials (2011)
450citations for 4 years
Li9.54Si1.74P1.44S11.7Cl0.3
Nature Energy (2016)
Tokyo Inst. Tech, KEK, TOYOTA, Ibaraki Pref.
1D diffusion path
3D diffusion path
（数分で充電）
Newspaper (Tokyo Newspaper (7/25), Chunichi News Paper (7/28))
TOYOTA will load all-solid buttery into Electric Vehicle in 2022
Neutron diffraction have revealed the diffusion path of ions, which is a key for development of new buttery materials.
Notes: 今回開発した全固体セラミックス電池は、電解液を用いるリチウムイオン電池よりはるかに高出力であることを実証した。これは、蓄電池の「大容量の電気をためる」性質と、キャパシタの「大電流を流せる」という異なる特徴を兼ね備えているため、画期的な電池といえる。

## Slide 26
High Pressure Science
Light Element in the Earth’s Core
Earth’s Core
・Main constituent :Fe-Ni Alloy
・Density of the outer core is smaller than that of Fe-Ni alloy
→Suggesting the existence of Light Elements, such as H, C, S, Si, O,....
What amount of hydrogen is involved?
How hydrogen is involved in the iron?
Notes: Here shows the cutaway view of the Earth. The Earth has the layered structure, consisting of crust, mantle, core from the top to bottom. From the density of each layer which is precisely determined from the velocity of the seismic wave, we can estimate the constituent of each layers. The core is known to be composed of Fe-Ni alloy, but the density is 10 % smaller than the alloy. This indicates that lighter elements such as hydrogen, carbon, sulfur, silicon and oxygen, is included in the core. Most promising candidate is hydrogen because H is the abundant element of the Earth. Therefore, it is important to know what amount of hydrogen is included and how the hydrogen is included in the iron.

## Slide 27
High-pressure Neutron Diffractometer PLANET (BL11)
Hydrogen in Fe lattice under high pressure and high temperature condition
Hydrogen in iron is directly related to hydrogen embrittlement of iron and the possible origin of the deficit in density of the Earth’s Core.
PLANET measured neutron diffraction from hydrogen (deuterium) in iron at high-PT condition (6.3 GPa and 988 K)
The structure analysis revealed that small amount of deuterium do occupy the tetrahedral site, contrary to conventional model where all the deuterium occupy the octahedral site. More hydrogen in Fe in Earth Core.
Nature Comm., 5, 5065 (2014).
Recently , they measured neutron diffraction from hydrogen (deuterium) in iron as a function of P and T to reveal the early stage of Earth’s evolution.
Large press “ATSUHIME”
PLANET on BL11
Nature Comm., 8, (2017)

## Slide 28
Summary
J-PARC MLF is moving from the construction phase to the Operation phase.
Operation of new target (#8) is very stable at 400 kW.
We will exchange the target to a new one (#10) in the summer shutdown 2018 and achieve 1MW in 2018.
Instruments have the world level performance, and still developing.
Developments of sample environments and new neutron devices are on-going.
Spin-echo machine was open to users @2017B
Polarization Analysis Spectrometer (POLANO) is under beam commissioning
We still continue to improve J-PARC MLF to increase high quality outcomes