## Slide 1: Target Design and Maintenance Scenario at ESS
Rikard Linander
Deputy Head of Target Division
www.europeanspallationsource.se
17 January, 2018

## Slide 2: Target Design and Maintenance Scenario at ESS Presentation outline
Design and Layout of the ESS Target Station and the main Target Systems
  Target Systems
  Moderator and Reflector Systems
  Neutron Beam Extraction System
  Remote Handling Systems
Maintenance Scenario Example: Exchange of a Neutron Beam Port Insert

## Slide 3: Design and Layout of the ESS Target Station and the main Target Systems

## Slide 4: Key features of the ESS Target Station
Helium cooling of target material
Mass flow 3 kg/s
Pressure 11 bar
Temperature inlet/outlet 40 °C/240 °C
proton beam
proton beam window
proton beam instrumentation plug
Moderator and reflector
target wheel
neutron beam extraction port
monolith vessel
target monitoring plug
Rotating solid tungsten target
36 sectors
Mass, total 11 tonnes, whereof 3 tonnes of W
Rotates 23.3 rpm, synchronized with pulsed proton beam 14 Hz
Moderators
Provisional locations of moderators above and beneath the target wheel, i.e. monolith centre
1st MR plug exploits the upper space, offering:
  Cold, 30 mm high, liquid H2 moderators, 17 K
  Thermal, 30 mm high, H2O moderator, 300 K
Diagnostics and instrumentation
Controlled and integrated commissioning and operation of the accelerator and target
Fluorescent coating of PBW and target front face
Optical paths, grid profile monitor, aperture monitor
Wheel monitoring including position, temperature, vibration, as well as internal structure
Target Safety System
Monitors target coolant flow, pressure and temperature, monolith pressure, & target wheel rotation
Prohibit beam on target if parameters are outside specified limits

## Slide 5: Key features of the ESS Target Station
Utilities and cooling plant
Helium cooling of target wheel
Water cooling of moderators, plugs and shielding
Intermediate water loops between primary circuits and conventional facility utilities
Helium cryoplant for refrigeration of cold moderator system
Nuclear grade HVAC system
130 m
22 m
37 m
High bay
Transport hall
Remote handling systems
Large active cells for safe storage and processing of spent radioactive target components
Shielded casks for transfer of spent components from monolith to active cells
Beam expander hall
Target monolith
Utilities block
Active cells

## Slide 6: Experimental Halls and Layout of Beam Lines and Neutron Science Instruments
6
Monolith
Neutron beam extraction
Offers 42 neutron beam ports
Allows neutron science instruments to view either upper or lower moderator position

## Slide 7: Target Systems

## Slide 8: ESS will be the first spallation source to employ a helium-cooled rotating target
Motor and bearings are mounted far away (5 meters) from the high radiation zone
  Wheel is suspended on a 6 meter long shaft
Helium removes 3 MW of heat deposited in the target by the 5-MW proton beam
Expected lifetime of 5 years
Wheel rotation scheme
  Target wheel has 36 sectors of 10° each
  The beam pulse is 2.86 ms wide, and pulses 14 times per second
  Wheel rotation is synchronized with the beam pulse
  Wheel rotational speed is14 Hz/36 = 0.39 Hz, or 10° rotation between each pulse
5 m
2.6 m

## Slide 9: Each 10° sector is loaded with a tungsten-filled cassette
48 cm
proton beam
Tungsten depth in the proton beam direction is 45 cm
The range of a 2-GeV proton in tungsten is 74 cm
Brick dimensions: 10 W x 30 D x 80 H mm3
190 bricks per sector, 6840 bricks in total
Helium flows
  radially outward above and below the cassette,
  reverses direction at the wheel rim,
  and returns through the tungsten
Tungsten bricks
Cassette
Target Wheel prototype

## Slide 10: Target Wheel and Helium Cooling System

## Slide 11: Moderator and Reflector Systems

## Slide 12: Main functions and design of the ESS Moderator and Reflector Systems
Moderate neutrons to low energies, thermal and cold, useful for the neutron scattering
Cooling the radiation heat in liquids and solid metal bodies
Cryogenic moderator prototype used for rupture test

## Slide 13: Moderator and Reflector Plug and Liquid Hydrogen Systems
Cryostat internals
One of three final cold moderator vessels, of which two will be used in the first MR plug
Cryogenic hydrogen system
Pre-milled raw material for the reflector vessels
Deep-hole drilled thermal moderator

## Slide 14: Target Wheel and Moderator and Reflector unit (MR Plug) placement in Monolith
Target Wheel
MR Plugs
Proton Beam

## Slide 15: Neutron Beam Extraction System

## Slide 16: Neutron Beam Port Insert Overview
The Neutron Beam Port Insert (NBPI) is part of the Neutron Beam Extraction System and is the in-vessel beam guide support structure.
Internal Neutron Beam Optics Assembly (NBOA)

## Slide 17: Interface to Neutron Scattering Systems
Instrument beam guide
Bunker roof
Bunker wall
Monolith wall
Notes: The bunker roof, part of NSS, has to be dismantled during insert changes.
The sequence when changing the insert will be more detailed in Naja’s presentation during the decommissioning of inserts.

## Slide 18: Neutron Beam Extraction View from Experimental Hall, No bunker shown, and transparent floor slab

## Slide 19: Neutron Beam Extraction system Shutter system in basement
Neutron Beam Port Insert (NBPI)
Neutron Beam Window (NBW):
Light Shutter System:
  Bridge Beam Guide (BBG) w optics,
  Gamma Beam Shutter (GBS) acts as safety system,
  Rail system.
RH Tooling:
  Horizontal of NBPI
  Vertical of BBG and NBW
BBG
NBW
GBS
Bunker roof support pillar
Handling tooling
Bunker floor
NBPI

## Slide 20: Remote Handling Systems

## Slide 21: Remote Handling Systems and Maintenance Logistics

## Slide 22: Remote Handling Systems
Casks
Active Cells Facility
MUTS
Active Cells Facility:
Length: 30 m
Depth: 12 m
Height: 15 m

## Slide 23: Maintenance Scenario Example: Exchange of a Neutron Beam Port Insert

## Slide 24: Exchange of a Neutron Beam Port Insert Removal of used item
Bunker preparations
  removal of roof
  sector cleared from Monolith boundary to Bunker wall.
Area is tented off.
Floor unit aligned on instrument baseplate.
Insert Extraction Tool (IET) is hoisted in.
Parallel LSS activities in basement - Dry and drain of NBPI.
Cold box arrival to ESS
Notes: The NBPI is still in the design phase so operational and maintenance aspects are in the same state.
Based on this reasoning - each NBPI is expected to be changed every 15 years. When we are up and running with all 42 ports this will mean a change of approximately three beam guides each year.
Port block surface is refurbished due to potential damage from NBW

## Slide 25: Vertical cross section of Monolith, NBPI and Insert Extraction Tool
NBPI
Notes: Extraction tool (ej IET)

## Slide 26: Exchange of a Neutron Beam Port Insert Removal of used item
Remote unbolting of NBW from basement.
Removal of NBW into cask.
Transport (of NBW) to Active Cell.
Refurbishment of port block surface – also remote from basement:
  Refurbishment is done while the NBPI is still in place to minimize particle introduction into the monolith.
Cold box arrival to ESS
Notes: The NBPI is still in the design phase so operational and maintenance aspects are in the same state.
Based on this reasoning - each NBPI is expected to be changed every 15 years. When we are up and running with all 42 ports this will mean a change of approximately three beam guides each year.
Port block surface is refurbished due to potential damage from NBW

## Slide 27: Exchange of a Neutron Beam Port Insert Removal of used item
IET docks on to NBPI.
NBPI is extracted.
IET is closed and undocks, hoisted up and transported to Bunker hand over point.
LSS activities initiates - GBS lowered to cover port opening.
IET is checked for surface contamination.
2nd generation NBPI can be installed.
IET lowered from handover point to horizontal transport by Experimental hall crane.
Transported to hatch in passageway between D01 and D03 for transfer to Active Cell.
Opening in bunker roof for NBPI exchange
IET

## Slide 28: Exchange of a Neutron Beam Port Insert Transfer to active cells facility
Hatch opened by High Bay crane.
IET hoisted up.
Floor valve adapter transported and put in place on Active Cell floor valve.
IET docks to floor valve adapter horizontally.
Rigid chain actuator is replaced by winch unit.
IET is tilted 90 degrees.
Valve and floor valve is opened.
NBPI is lowered into Active Cell and disconnected.
Active Cell takes over responsibility for NBPI, cut the NBPI and package it for transport off site.

## Slide 29: Exchange of a Neutron Beam Port Insert Removal and transfer sequence in pictures