## Slide 1: 2nd DMSC - Detector Group Readout Meeting
Morten Jagd Christensen
European Spallation Source
Data Management and Software Centre (DMSC)
Copenhagen

## Slide 2: Topics
Documentation/Process
Design/Implementation
  Readout protocol
Considerations
  Readout ‘load balancing’

## Slide 3: Documentation/Process
Where do we put this stuff?
  Temporary(?) Wiki page created with initial encapsulation suggestion (may 2017)
  Some comments and requests have been added
Is this the right format?
Is it sufficiently detailed currently?
  New data types needed (?) - pulse time, heartbeat
  (Addressing, packet sizes,...)
How do we work on it?

## Slide 4: Design/Implementation
Have
  Outline of packet encapsulation
  Promise of 100G data transmission
Would like
  discussion of DG TX / DMSC RX interface
  detailed network topology and addressing discussions
  new data types (?)
  ideas/specifics of the expected processing hardware for DMSC

## Slide 5: Consideration: Speed up
- by parallelisation
General solution
  distribute readouts across multiple EFU’s
  distribute readouts to a EFU across multiple queues
  can have implications for design of readout backend

## Slide 6: Considerations: Data path
Topology
  A readout master sends to one or more EFUs
  EFUs receive from one or more RO Masters
How to get the relevant readout data to the right destination?
  mapping ‘channels’ to IP/UDP destinations
  a single IP/UDP port may not be sufficient
Duplication?
  ‘overlapping’ regions, can they be transmitted to multiple receivers?

## Slide 7: Speed up by parallelisation
Some detectors are easy
  Multiblade - blades are independent
  Multigrid – grid stacks are independent
  SoNDe – comes as detector pixels (more or less)
  DREAM – comes as detector pixels (more or less)
At least one is complicated
  Gd-GEM – panels are independent, but cannot easily be segmented

## Slide 8: NMX Speedup

## Slide 9: Readout Data Paths
readout
CPU00
CPU01
CPU02
ch1
ch2
ch3
ch4
ch5
ch6
static ip
readout
CPU00
CPU01
CPU02
CPU00
CPU01
CPU02
ch1
ch2
ch3
ch4
ch5
ch6
dynamic ip mapping

## Slide 10: Readout Data Paths
readout
ch1
ch2
ch3
ch4
ch5
ch6
static ip, dynamic port mapping
dynamic ip and port mapping
CPU00
CPU01
CPU02
CPU03
CPU04
readout
ch1
ch2
ch3
ch4
ch5
ch6
CPU00
CPU01
CPU02
CPU03
CPU04
CPU00
CPU01
CPU02
CPU03
CPU04

## Slide 11: Single Detector Panel
CPU00
CPU01
CPU02
CPU03
CPU04
CPU05
CPU06
CPU07
CPU08
CPU09
CPU10
CPU11
Intel x86_64CPU
NMX panel, VMM3 readout
NMX panel, VMM3 readout
readout

## Slide 12: Single Detector Panel
CPU00
CPU01
CPU02
CPU03
CPU04
CPU05
CPU06
CPU07
CPU08
CPU09
CPU10
CPU11
Intel x86_64CPU
NMX panel, VMM3 readout
NMX panel, VMM3 readout
readout

## Slide 13: Wish list for the collaboration
Roadmap for the DG/DMSC interface
Roles and responsibilities
Early detector readout prototype
  first expected instrument, easiest implementation or most common readout technology (vmm?)
Documentation